## Slide 1: Approximate Fair Control-delay (AF-CODEL) Queue over High-speed Networks
Lin Xue
Nov.2012

## Slide 2: Challenge in High Speed Networks
Long-delay high-bandwidth
  To get high throughput in the order of 10Gbps
  Queuing delay could be huge (sometimes 120ms!)
Fairness problem
  People are using different TCP variants
  Non-responsive flows (85% TCP, 15% UDP in internet2)

## Slide 3: Queue Management Schemes
FIFO
RED
SFB(Stochastic Fair Blue)
  Identify and rate-limit non-responsive flows
AFQ(Approximate Fair Dropping)
  Provide approximate fairness
CODEL(Control Delay Queue)
  Recently proposed, control queuing delay

## Slide 4: Motivation
AQMs are proposed to achieve some goals:
  RED for early detect congestion
  SFB for detect non-responsive flow
  AFQ for fairness
  CODEL for low latency
However, non of the AQM could provide all of following in high-speed networks:
  High throughput
  Fairness
  Low latency

## Slide 5: Throughput and Fairness Problem
Chart: Queue Management Schemes 1 CUBIC flow and 1 RENO flow competing in the bottleneck Unfairness for heterogeneous TCPs! AFQ approximately solves fairness problem
| FIFO | RED | SFB | CODEL | AFQ
CUBIC flow | 7.52 | 6.63 | 4.68 | 6.97 | 3.9
RENO flow | 0.5 | 0.4 | 1.38 | 0.3 | 3.2

## Slide 6: Throughput and Fairness Problem 2
Chart: Queue Management Schemes 1 CUBIC flow and 1 Non-responsive UDP flow competing in the bottleneck TCP flow starvation! AFQ and SFB are good to detect non-responsive flow!
| FIFO | RED | SFB | CODEL | AFQ
CUBIC flow | 0.03 | 0.02 | 3.32 | 0.02 | 3.64
UDP flow | 7.62 | 7.79 | 3.99 | 7.83 | 3.67

## Slide 7: Delay Problem
Chart: Queue management schemes CODEL works great for control delay!
| FIFO | RED | SFB | CODEL | AFQ
1 CUBIC 1 RENO | 100 | 12 | 45 | 1 | 15
1 CUBIC 1 UDP | 120 | 20 | 60 | 1 | 35

## Slide 8: Summary of Problems
AFQ works good for fairness (SFB also works good for fairness in non-responsive flow case)
CODEL works good for delay

## Slide 9: Approximate Fair CODEL Queue
None of current AQMs works good for both fairness and delay!
Solution: AF-CODEL queue
Combine AFQ and CODEL to provide good solution for fairness and low latency, while do not hurt link utilization!

## Slide 10: Mechanism of AFQ
Packet enqueue
Sample packet
(sample interval 1/500 packets)
Update shadow buffer(SB, size 2000) and flow table (FT, size 100)
Drop decision
based on fair share information from SB and FT
Y
N
Drop
Enqueue
Y
N

## Slide 11: Mechanism of CODEL
Packet dequeue
Within interval(100ms)
Min Queuing delay > target(5ms)
Drop
Dequeue next packet
Schedule next drop
Stop drop
Y
N

## Slide 12: Mechanism of AF-CODEL
AFQ mechanism is at enqueue
CODEL mechanism is at dequeue
Combine them together